## Slide 1: PoE Passthrough Proposal
Brandon Beader & Diang Xing
8/30/2023

## Slide 2: Contents
TI PoE Portfolio
  PD Section
  PSE Section
Passthrough (daisy chaining)
  Benefits of passthrough
  Block diagram
  TI solutions for PoE daisy chaining
Device Information
  TPS23881B1
  TPS2372-3

## Slide 3: TI PoE Portfolio

## Slide 4
Power level
≤ 71.3W (Class 5-8)
≤ 25.5 W
(Class 4)
Isolated or Non-Isolated?
Isolated
Non-Isolated
TPS23758
<13W (Class 1-3)
Isolated
Design?
Y / Flyback
(Recommended)
Vout level?
3.3V/5V
TPS23755
(Smooth Transition w. AUX)
N / Buck
>=12V
Isolated Design?
TPS2372
(Also for dual input)
Y / Flyback
TPS2373 - 4
(Generally more recommended than TPS2372)
N / Buck
NEW
TPS23731
NEW
TPS23734
TPS2378
Which Topology?
ACF
Flyback
TPS23753A
Primary or Secondary side Regulation?
Primary
Secondary(w/ Opto)
NEW
TPS23730
Power Level<=51W
YES
NO
Isolated Design?
Y / Flyback
or ACF
N / Buck
PoE PD Selection Flowchart

## Slide 5: PSE selection flowchart
Power level > 30 W ?
YES
NO
TPS23881
8 channel
FirmPSE compatible
Need more than 4 channels?
NO
YES
TPS23861
4 channel
Autonomous mode included
TPS23882
8 channel
FirmPSE compatible
TPS23882B1
8 channel
FirmPSE compatible
Autonomous mode included
OR
Autonomous mode
No host controller or system software needed
Best for systems where supply can support all ports on max load
TPS23881B1
8 channel
FirmPSE compatible
Autonomous mode
OR
RTM’d
In development

## Slide 6
PD Featured Reference Designs
13 W
51 W
71 W
25 W
5 V
12 V
Powered device (PD) input power
Output voltage level
TPS2373-4EVM-758
TPS23758EVM-080
TPS23731EVM-095
Synchronous flyback
TPS23734EVM-094
TIDA-050045 ACF
PMP22806
TPS23755EVM-894
TPS23754EVM-383
PMP22477
TPS23730EVM-093
Cost Optimized
High Efficiency
Standard
PMP21318
Find interactive table here
3.3 V
> 12 V
PMP20878
ACF
TIDA-00539
Flyback
PMP22301
Flyback
PMP7452
ACF
PMP10288
ACF
TPS23753AEVM-004 Flyback

## Slide 7: Passthrough (Daisy Chaining)

## Slide 8: PoE Daisy-Chaining Overview
IoT end equipment have been focused on solving system level solutions. For example, WAPs that can power IP cameras. Or lighting systems with people counting sensors.
100m of CAT5e cable may not be long enough to deliver both data and power to end equipment.
PoE daisy chaining can help solve this these issues by chaining multiple PDs that have different functionalities and daisy chaining helps extend the ethernet cable length past 100m.
The current PoE standard limits power level and so limits daisy chaining capabilities. However the new IEEE802.3bt standard will increase power levels and help enable these solutions.
Key considerations are maintaining interoperability using TI’s IEEE802.3bt ICs and understanding the power distribution is a PoE system.

## Slide 9: PoE Pass-Through Applications
Wireless Access Points
Smart Parking Garages
Audio Belt Packs
Enterprise switch Adapters
Conference Room Hubs

## Slide 10: High Level Block Diagram: PoE Pass-through
PD
TPS2372-3
PSE
TPS23881B1
PD Load
5W
54V
PD
TPS2372-3
PSE
TPS23881B1
PD Load
5W
54V
Device 2
Device 3
Device 1
Device 4

## Slide 11: Multi-system Daisy Chain
PD
PSE
Output
Device 1
Power Source
PSE
PD
Device 2
PSE
PD
Device 3
PSE
PD
Device 4
PSE
Host
PD
PSE
PD
PSE

## Slide 12: Multi-system Daisy Chain
PD
PSE
Device 1
Power Source
PSE
PD
Device 2
PSE
PD
Device 3
PSE
PD
Device 4
PSE
Host
PD
PSE
PD
PSE
IEEE802.3bt PSE/PD needed due to total power consumption of 6 device system:
6x 5W Loads (30W) total load
100m cable Loss between devices
>30W requires IEEE802.3bt Type 3-4 PSE/PD
Up to 90W
5W Load
5W Load
5W Load
5W Load
5W Load
5W Load
Loss
Loss
Loss
Loss
Loss
Loss
Total Load >30W

## Slide 13: Considerations
Due to total daisy chain system load >30W, a IEEE802.3bt Type 3-4 PSE/PD setup is required.
  This is mainly due to local load consumed at device + cable loss
TPS23881B1 will RTM end of October. This device can support up to 90W without need for host control.
  If wish to due dynamic passthrough (active power monitoring, please see slides 19-23), host control is needed
  TPS23881B1 supports autonomous mode, also supports host control.

## Slide 14
Set to Class 4 and Class 4
Connect VDD on TPS2372EVM to (+) on TPS23881EVM
Connect RTN on TPS2372EVM to (-) on TPS23881EVM
PD Input
PSE output

## Slide 15: TI - Device Architecture
44-57V
PD
TPS2372-3
PSE
TPS23881B1
PD Load
5W
Device 1
FET Bridge
RJ45
Buck
LM5116
RJ45
Device 2
LDO (TLV760)
5V
3.3V
Vdd
Vpwr
44-57V
44-57V
Autonomous mode:
No host controller needed in order to passthrough

## Slide 16: Static PoE Pass Through

## Slide 17: Static PoE Pass-Through
PD
Input
PSE
Output
PD Load
54V
PD
Input
PSE
Output
PD Load
54V
System designer knows the number of daisies, and cable lengths, and input power:
Back-calculate how long the chain can be
  PD voltage at the last chain is above the UVLO threshold of the PD controller
Limit total solution within those system requirements
Vdrop1
Efficiency hit 1
Vdrop2
Efficiency hit 2

## Slide 18: Dynamic PoE Pass Through

## Slide 19: Architecture Proposal for 2 PSE ports
TPS2372-3
TPS23881B1

## Slide 20: Determining what’s connected to the PD
PSE Type | Power Sourced from PSE (W) | Maximum Power at PD (W) | Class Signature A | Class Signature B | Number of Class Cycles | Resistor CLSA | Resistor CLSB | TPH | TPL | /BT
1-2 | 15.4W | 13.0W | 0 | 0 | 1 | 1210 | 1210 | HIGH | HIGH | HIGH
1-2 | 4W | 3.84W | 1 | 1 | 1 | 249 | 249 | HIGH | HIGH | HIGH
1-2 | 7W | 6.49W | 2 | 2 | 1 | 140 | 140 | HIGH | HIGH | HIGH
1-2 | 15.4W | 13.0W | 3 | 3 | 1 | 90.9 | 90.9 | HIGH | HIGH | HIGH
2 | 30W | 25.5W | 4 | 4 | 2 | 63.4 | 63.4 | HIGH | LOW | HIGH
3-4 | 15.4W | 13.0W | 0 | 0 | 1 | 1210 | 1210 | HIGH | HIGH | LOW
3-4 | 4W | 3.84W | 1 | 1 | 1 | 249 | 249 | HIGH | HIGH | LOW
3-4 | 7W | 6.49W | 2 | 2 | 1 | 140 | 140 | HIGH | HIGH | LOW
3-4 | 15.4W | 13.0W | 3 | 3 | 1 | 90.9 | 90.9 | HIGH | HIGH | LOW
3-4 | 30W | 25.5W | 4 | 4 | 2-3 | 63.4 | 63.4 | HIGH | LOW | LOW
3-4 | 45W | 40.0W | 4 | 0 | 4 | 63.4 | 1210 | LOW | HIGH | LOW
3-4 | 60W | 51.0W | 4 | 1 | 4 | 63.4 | 249 | LOW | HIGH | LOW
4 | 75W | 62.0W | 4 | 2 | 5 | 63.4 | 140 | LOW | LOW | LOW
4 | 90W | 71.3W | 4 | 3 | 5 | 63.4 | 90.9 | LOW | LOW | LOW
Adapter (APD HIGH) | NA | NA | NA | NA | NA | NA | NA | LOW | HIGH | HIGH
POE++ | 45 | 38.7 | 4 | 0 | 3 | 63.4 | 1210 | LOW | LOW | HIGH
POE++ | 65 | 52.7 | 4 | 1 | 3 | 63.4 | 249 | LOW | LOW | HIGH
POE++ | 90 | 70 | 4 | 2 | 3 | 63.4 | 140 | LOW | LOW | HIGH
POE++ | 123 | 90 | 4 | 3 | 3 | 63.4 | 90.9 | LOW | LOW | HIGH

## Slide 21: TPH TPL BT Measurements
Actual Resistance

## Slide 22: DCDC Input Voltage/Current Measurements
Current
Voltage

## Slide 23: Passthrough Device Information

## Slide 24
Ethernet Switches and Routers
Lighting
Pass-through Systems
SOHO Routers
Ethernet Hubs
Applications
Features
Benefits
8 x 8 mm, 56-pin
QFN package
TPS23881B1 8-Channel 802.3bt Type-4 PSE w/ SRAM
IEEE 802.3bt interoperability
Flexible solution can deliver beyond .bt power levels
Firmware upgradability
Expand max power sourced to 95W w/o exceeding 100W
High current sensing accuracy and low power dissipation
Detect & power legacy PDs
Enables PSE systems without a host or I2C communication
Required for PoE lighting applications
Ability to detect and power dual signature PD loads.
IEEE 802.3bt Ready
2-Pair (up to 30W) & 4-Pair (up to 125W) Configurable
I2C Programmable SRAM
Programmable power limiting accuracy ±2.5%
0.200 Ω Sense Resistor with Kelvin Sensing
Legacy PD Capacitance Measurement
Autonomous Mode
Autoclass Detection and Power Measurement
Single & dual signature PD compatibility
Fast port shutdown input w/ up to 8 priority settings
Short-Circuit Protection with Foldback
14-Bit Port Current and Voltage Monitoring
Ultra Low Alpha Packaging Available (TPS23881A)
Est. ETM Oct. ‘23

## Slide 25: TPS2372-3/TPS2372-4 High Power .bt PoE PD Interface with MPS and Low Standby Power
Features
Compliant PD I/F for 2- and 4-pair applications
High Power Robust Solution up to 90W and 60W
Allows Ultra-high “light load” efficiency solutions
  Ensures PSE will maintain power at any load
Allows optimum PSE power budgeting
No Interoperability issue with PSE during inrush
Benefits
PoE Lighting
4-Pair Non-isolated PoE
Wireless Access Points
IP cameras
Applications
IEEE 802.3bt, at and UPOE solution
Robust 100 V Hotswap MOSFET
  TPS2372-4 (typ.): 0.1-Ω, 2.2-A Current Limit
  TPS2372-3 (typ.): 0.3-Ω, 1.8-A Current Limit
Automatic Maintain Power Signature
Supports Autoclass
PG Output with PSE Inrush Completion delay
QFN20 Package (5x5 RGW)
Notes: 25